## Slide 1
AGRO-CLIMATIC AND HYDROLOGICAL CHARACTERIZATION OF SELECTED WATERSHEDS OF NORTHERN GHANA
Kadyampakeni et al.
International Water Management Institute

## Slide 2: Introduction and objectives
Agriculture is the mainstay of livelihoods of people in northern Ghana
There is enormous potential for expanding irrigated and cropped area through irrigation and other agricultural interventions
Aim: To develop baseline information for intended water management interventions for agricultural intensification in three watersheds in northern Ghana (Anyari, Zanlerigu and Bihinaayili).
Watershed | Communities
Anyari | Nyangua, Dimbasinia, Tekuru
Zanlerigu | Zanlerigu
Bihinaayili | Bihinaayili, Duko

## Slide 3: Research approach
Baseline information collected on watershed boundary, soil types, land cover
Analysing climatic data (Navrongo, Tamale and Zuarungu stations)
  Dry spells
  Rainfall deficit
Field visits collecting information on
  Validation of agricultural systems (focus group discussion
  Water quality of selected water sources (see table) and soil chemical properties of farm lands to assess their suitability for irrigation
Desktop study was conducted to obtain secondary data and information on the hydrological, climatic and agricultural systems.

## Slide 4: Main results and discussion
Seasonal rainfall 989-1012 mm/yr
No significant trends observed except for increasing trend for PET in the Bihinaayili watershed.
Only 3 months per year does rainfall exceed PET
Dry spells of 7-days or more occurs more than 80% of the time
On-field water management in combination with supplemental irrigation or installation of water storage technologies in the rain-fed systems can mitigate the impact of dry spells to improve yield levels.
 | Navrongo | Zuarungu | Tamale
7-day (%) | 81.25 | 80.30 | 89.80
14-day (%) | 4.17 | 15.15 | 12.24
21-day (%) | 2.08 | 6.06 | 0.00

## Slide 5: Main results and discussion
Water quality (water sources)
Higher concentrations of parameters are found in wells than in surface water bodies
High Potassium concentrations are found across sites, associate with slash and burn practices by farmers
Higher concentrations found in April compared to October
Soil quality (farmer field plots)
Low organic carbon levels
pH levels in Bihinaayili, Nyangua and Tekuru are slightly acidic
Low nutrients; need for integrated soil fertility management

## Slide 6: Main results and discussion
Three cropping systems are practiced
  mixed cropping (not in Anyari),
  inter-cropping, and
  crop rotation
Irrigation in the three sites is done between December-June.
Sources of water
 | Anyari | Zanlerigu | Bihinaayili
Surface water | Two small reservoirs (25,000m3) –fall dry at the end of the season | Small reservoir 20,000 m3 – does not fall dry (higher concentrations) | Libga reservoir (5.8 Mm3) - perenial
Groundwater | Shallow wells | Shallow wells | Shallow wells (domestic)

## Slide 7: Conclusion
The three watershed are highly suitable for agricultural water management interventions
  Utilizing various water source, shallow wells and small reservoirs with good water quality
  Soil is conducive but will require integrated management of soil fertility
High probability of dry spell occurrences affecting rainfed farming systems
  Better on-field water management in combination with supplemental irrigation or installation of water storage technologies needed to improve yield levels.
For successful sustainable intensification, farmers need support in developing appropriate agricultural water management strategies to attain productivity.